SPORT CALIBRATION

CHECKLIST

w/ GEAR WARN

Cklst gear.doc       05/01     rev 3

The POST INSTALLATION and HANGAR CALIBRA-TION check lists must be completed prior to flight.  The zero “G” maneuver requires that all unsecured items be removed from the aircraft prior to flight.  Two pilots are required during the calibration process and one must be assigned the task to fly the aircraft and nothing more.  The flight calibration area will be cleared for traffic and will be at a safe altitude with the IAS always within the green IAS band.  Stalls are not required or desired!

Switch activation is done by pushing and holding the designated colored switch for 1 second, then releasing the switch.  To get into the calibration mode, momentarily hold both the black and red switch pushed, then release both at the same time.

There are three modes, Flight, Self Test and Calibration.

In the Calibration mode, there are five pages.  Page Hangar Calibrate sets the pressure transducer zero offsets.  Page Zero "G" is where the no lift data is recorded.  Page Angle Advisory is where the "angle push" warning is set.  Page Landing Gear is where the "landing gear warning speed" is set.  Page Save is how data is stored to permanent memory.

Cruise Configuration is with gear, flaps and slats up.  Landing Configuration is with the gear, flaps and slats down for landing.  In the Flight mode, the black switch is the dimmer and the red switch is the push to test.  In the Self Test mode the buttons are inactive.  In the Calibrate mode, the red switch is the record data switch and the black switch is the skip to next page button without recording.

POST INSTALLATION PRE FLIGHT

Blow into Blue tube at CPU	Air exits Upper Wing Port

Blow into Green tube at CPU	Air exits lower Wing Port

Blow into Red tube at the CPU	IAS increases

Suck on Clear tube at the CPU	Altimeter increases

PITOT/STATIC LEAK TEST	COMPLETED

AIRCRAFT LOG	UPDATED

AIRCRAFT CHECKLISTS	UPDATED

ANNUAL CONDITION C/L	UPDATED

CHAPTER IX TESTING	COMPLETED

HANGAR CALIBRATION

Aircraft Location	Hangar

Gear SW	DOWN

AOA Power	ON

AOA Self Test	PASSED or ERRORS

RED/BLACK SW	PUSH BOTH/RELEASE

PAGE  hangar calibrate	All LEDs flash

RED SW  record	PUSH/RELEASE

BLACK SW skip 3 pages	3x PUSH/RELEASE

PAGE save data to permanent memory?	Odd LEDs flash

RED SW  Yes record	PUSH/RELEASE

AOA Power	OFF

CRUISE DATA CALIBRATION

AIRCRAFT LOCATION	SAFE ALTITUDE

AOA Power On 	ERRORS 11, 12 & 33

FLAPS/GEAR	 CONFIRMED UP

RED/BLACK SW	PUSH BOTH/RELEASE

PAGE  hangar calibrate	All LEDs flash

BLACK SW skip don't record	PUSH/RELEASE

PAGE  zero lift	 Bottom Green LED flash

Zero “G” Maneuver 1/2 sec.	ANY SAFE IAS

RED SW record	PUSH/RELEASE

PAGE  angle advisory	Bottom 6 LEDs flash

AIRSPEED 1.15Vs1 descending slow flight	YES

RED SW record	PUSH/RELEASE

BLACK SW  skip gear page	PUSH/RELEASE

PAGE  save cruise data to memory?	odd LEDs flash

RED SW Yes, record	PUSH/RELEASE

LANDING DATA CALIBRATION

AIRCRAFT LOCATION	SAFE ALTITUDE

FLAPS/GEAR	 CONFIRMED DOWN

RED/BLACK SW	PUSH BOTH/RELEASE

PAGE  hangar calibrate	All LEDs flash

BLACK SW  skip don't record	PUSH/RELEASE

PAGE  zero lift	 Bottom Green LED flash

Zero “G” Maneuver 1/2 sec.	ANY SAFE IAS

RED SW record	PUSH/RELEASE

PAGE  angle advisory	Bottom 6 LEDs flash

AIRSPEED 1.15Vso descending slow flight	YES

RED SW record	PUSH/RELEASE

BLACK SW  skip gear page	PUSH/RELEASE

PAGE  save landing data to memory?	odd LEDs flash

RED SW Yes, record	PUSH/RELEASE

LANDING GEAR WARN CALIBRATION

AIRCRAFT LOCATION	SAFE ALTITUDE

FLAPS/GEAR	 CONFIRMED DOWN

RED/BLACK SW	PUSH BOTH/RELEASE

PAGE  hangar calibrate	All LEDs flash

BLACK SW skip to LG page	3x PUSH/RELEASE

PAGE  landing gear	Bottom 3 LEDs flash

AIRSPEED	Vapproach + 15 knots

RED SW record	PUSH/RELEASE

PAGE  save data to memory?	odd LEDs flash

RED SW Yes, record	PUSH/RELEASE

FLAPS/GEAR	 CONFIRMED UP

RED/BLACK SW	PUSH BOTH/RELEASE

BLACK SW skip to save page	4x PUSH/RELEASE

PAGE  save data to memory?	odd LEDs flash

RED SW Yes, record	PUSH/RELEASE

FLIGHT TEST AOA

VERIFICATION C/L	COMPLETE

CHAPTER X CALIBRATING	COMPLETE

CHAPTER X FLIGHT TESTING 	COMPLETE

FLY THE AIRPLANE & watch for traffic!